## Slide 1: Anatomy of a Large European IXP
Anja Feldmann
TU Berlin/T-Labs
Walter Willinger
AT&T Labs Research
Nikos Chatzis Nadi Sarrar
TU Berlin/T-Labs
Steve Uhlig
Queen Mary
University of London
Bernhard Ager ETH Zürich

## Slide 2: IXPs – Reminder…
Accepted industry definition of an IXP (according to Euro-IX):
  A physical network infrastructure operated by a single entity with the purpose to facilitate the exchange of Internet traffic between Autonomous Systems.
  The number of Autonomous Systems connected should at least be three and there must be a clear and open policy for others to join.
https://www.euro-ix.net/what-is-an-ixp

## Slide 3: Infrastructure of an IXP (DE-CIX)
http://www.de-cix.net/about/topology/
Robust infrastructure with redundency

## Slide 4: Internet eXchange Points (IXPs)
Layer-2 switch
AS4
Content
Provider 2
AS5
AS1
AS2
Content
Provider 1
AS3
IXPs
Offer connectivity to ASes
Enable peering

## Slide 5: IXPs – Peering
Peering – Why? E.g.: Giganews:
  “Establishing open peering arrangements at neutral Internet Exchange Points is a highly desirable practice because the Internet Exchange members are able to significantly improve latency, bandwidth, fault-tolerance, and the routing of traffic between themselves at no additional costs.”
IXPs – Four types of peering policies
  Open Peering – Inclination to peer with anyone, anywhere
    Most common!
  Selective Peering – Inclination to peer, with some conditions
  Restrictive Peering – Inclination not to peer with any more entities
  No Peering – No, prefer selling transit
http://drpeering.net/white-papers/Peering-Policies/Peering-Policy.html
Notes: 240 Open Peering policy
Restrictive
126 Restrictive
49 Unknown

## Slide 6: IXPs – Publicly available information
Sources: euro-ix, PCH, PeeringDB, IXP’s sites
Generally known: # IXPs ~ 350 worldwide
http://www.pch.net

## Slide 7: IXPs – Publicly available information
Chart: 
| AMS-IX | DE-CIX Frankfurt | LINX | MSK-IX | NL-ix | PTT.br | NOTA | PLIX | Equinix Paris | Equinix Zurich | Any2 (CoreSite) | SwissIX
ASNs at IXP | 499 | 450 | 442 | 367 | 284 | 284 | 267 | 203 | 176 | 176 | 147 | 142
Unique ASNs | 78 | 79 | 95 | 272 | 134 | 171 | 174 | 160 | 0 | 0 | 60 | 85
https://www.euro-ix.net
Generally known: # IXPs ~ 350 worldwide
Somewhat known: # ASes per IXP up to 500

## Slide 8: IXPs – Publicly available information
Chart: IXP Member ASes by region
| Europe | North America | Asia/Pacific | Latin America | Africa
IXP Participants | 6622 | 2155 | 1502 | 560 | 160
https://www.euro-ix.net/tools/asn_search
Generally known: # IXPs ~ 350 worldwide
Somewhat known: # ASes per IXP up to 500
Less known: # ASes ~ 11,000 worldwide

## Slide 9: IXPs – Publicly available information
Generally known: # IXPs ~ 350 worldwide
Somewhat known: # ASes per IXP up to 500
Less known: # ASes ~ 11,000 worldwide
Even less known: IXPs =~ Tier-1 ISP traffic
Chart: 
| Aug 2008 | Sep 2008 | Oct 2008 | Nov 2008 | Dec 2008 | Jan 2009 | Feb 2009 | Mar 2009 | Apr 2009 | May 2009 | Jun 2009 | Jul 2009 | Aug 2009 | Sep 2009 | Oct 2009 | Nov 2009 | Dec 2009 | Jan 2010 | Feb 2010 | Mar 2010 | Apr 2010 | May 2010 | Jun 2010 | Jul 2010 | Aug 2010 | Sep 2010 | Oct 2010 | Nov 2010 | Dec 2010 | Jan 2011 | Feb 2011 | Mar 2011 | Apr 2011 | May 2011 | Jun 2011 | Jul 2011 | Aug 2011 | Sep 2011 | Oct 2011 | Nov 2011 | Dec 2011 | Jan 2012 | Feb 2012 | Mar 2012 | Apr 2012 | May 2012 | Jun 2012
Bytes In | 89760 | 95562 | 109978 | 120295 | 127158 | 135305 | 127811 | 139914 | 129176 | 136618 | 136004 | 133002 | 138643 | 150898 | 169015 | 173557 | 179905 | 186950 | 177486 | 197278 | 188311 | 201093 | 187804 | 186283 | 198972 | 209658 | 232111 | 236639 | 254300 | 261958 | 243915 | 262317 | 247194 | 261466 | 260585 | 261666 | 263888 | 260055 | 295135 | 295556 | 301413 | 316081 | 296047 | 312935 | 318352 | 318661 | 314126
AMS-IX
Total TB in

## Slide 10: IXPs – Publicly available information
Generally known: # IXPs ~ 350 worldwide
Somewhat known: # ASes per IXP up to 500
Less known: # ASes ~ 11,000 worldwide
Even less known: IXPs =~ Tier-1 ISP traffic
Unknown: # of peerings at IXPs
Notes: 5 minutes

## Slide 11: Peering links – current estimates?
Methodology | Number of peering links in the entire Internet
[Dhamdhere et al.] 2010 Lower bound estimate based on BGP data) | > 20,000

## Slide 12: Peering links – current estimates?
Methodology | Number of peering links in the entire Internet
[Dhamdhere et al.] 2010 Lower bound estimate based on BGP data) | > 20,000
[Augustin et al., Chen et al.] 2009/2010 Targeted/opportunistic traceroute from network edge | > 40,000
Dasu 2011. Targeted data plane measurements | > 60,000

## Slide 13: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Discussion
Summary

## Slide 14: Data – From collaboration with IXP
Major European IXP
9 month of sFlow records collected in 2011
Sampling 1 out of 16K packets
128 bytes  IP/TCP/UDP headers
Consistency checks and filters
  Checked for duplicates
  Filtered out IXP management traffic, broadcast and multicast (except ARP)
  Eliminated IPv6 (less than 1% of traffic)
Thanks to the IXP for a great collaboration!

## Slide 15: Fact 1 – IXP members/participants
 | Apr 25 May 1 | Aug 22 Aug 28 | Oct 10 Oct 16 | Nov 28 Dec 4
Member ASes | 358 | 375 | 383 | 396
Tier-1 | 13 | 13 | 13 | 13
Tier-2 | 281 | 292 | 297 | 306
Leaf | 64 | 70 | 73 | 77
Countries of member ASes | 43 | 44 | 45 | 47
Continents of member ASes | 3 | 3 | 3 | 3
Daily avg. volume (PB) | 9.0 | 9.3 | 10.3 | 10.7
Traditional classification

## Slide 16: Fact 2 – IXP members/participants
  Member ASes often offer multiple services
By Business type

## Slide 17: Fact 3 – IXP traffic
  Traffic Volume: Same as Tier-1 ISPs
  IXP is interchange for Tier-2 ISPs

## Slide 18: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Discussion
Summary
Notes: 10 minutes

## Slide 19: Fact 4 – IXP peerings
IXP peering link between pair of ASes if
  IP traffic exchanged
    BGP traffic only (e.g., in case of backup links)
    IP otherwise
Potential links
  Member ASes in Nov/Dec’11: 396
  396x395 / 2 = 78,210 P-P links possible
Observed links
  > 50,000 peering links
  Peering rate > 60%!
  June’12: 421
  > 55,000 peering links!
  Peering rate > 60%! > 60%!

## Slide 20: Fact 4 – IXP peerings Internet-wide
Single IXP > 50,000 peering links
Derivation of new lower bound
  10 large IXPs in Europe: ~160,000 peering links
  Remaining 340 or so IXPs: ~ 40,000 peering links
  Completely ignoring all other peerings
(Conservative) lower bound on #of peering links
  > 200,000 peering links in today’s Internet (as compared to currently assumed ~ 40,000 – 60,000)
Requires a revamping of the mental picture our community has about the AS-level Internet.

## Slide 21: Fact 4 – IXP peerings Internet-wide
Methodology | Number of peering links in the entire Internet
[Dhamdhere et al.] 2010 Lower bound estimate based on BGP data) | > 20,000
[Augustin et al., Chen et al.] 2009/2010 Targeted/opportunistic traceroute from network edge | > 40,000
Dasu 2011. Targeted data plane measurements | > 60,000
2012 (This talk) data from IXPs | > 200,000

## Slide 22: Public view of IXP peering links
  Peering links at IXP: > 50 K
  How come that we did not see them?
Dataset | Unique ASes with vantage points | Peerings
Routeviews (RV) | 78 | 
RIPE | 319 | 
Non public BGP (NP) | 723 | 
BGP (RV+RIPE+NP) | 997 | ~ 20-30 K
Traceroute (LG) | 148 | ~ 40-45 K
RV+RIPE+NP+LG | 1,070 | 

## Slide 23: Visibility of IXP peerings
  Even with all available datasets about 70% of IXP peering links remain invisible!
  Even with all available datasets about 43 % of exchanged bytes remain invisible!

## Slide 24: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Discussion
Summary
Notes: 15 minutes

## Slide 25: Member diversity – Business type
Classified ASes according to business model
For the remainder of this talk
  Large ISPs (LISP)
  Small ISPs (SISP)
  Hosters and CDNs (HCDN)
  Academic and enterprise networks (AEN)
  All business models present
  Recall: Most member ASes offer multiple types

## Slide 26: Member diversity – # of peers
  Most members have a large # of peers

## Slide 27: IXP – Fraction of Web-traffic
  Individual ASes differ significantly!

## Slide 28: IXP – Traffic asymmetry
  Individual ASes differ significantly!

## Slide 29: IXP – Geographic distance
  Individual ASes differ significantly!

## Slide 30: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Discussion
Summary

## Slide 31: Daily pattern – Top-10 tier-2 members
  Pronounced time of day effects
  Top 10 tier-2 responsible for 33% of traffic
  Some ASes fully utilize their capacity

## Slide 32: Structural properties of traffic matrix
  Use SVD to understand traffic matrix rank Energy in first k singular values
  22 values suffice for 95% of the energy
  Even smaller k for application specific matrix

## Slide 33: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Discussion
Summary
Notes: 20 minutes

## Slide 34: Internet: Mental model (before 2010)
http://conferences.sigcomm.org/sigcomm/2010/slides/S3Labovitz.pdf

## Slide 35: Most recent mental model – a 2011
  Flattening of the AS topology
http://conferences.sigcomm.org/sigcomm/2010/slides/S3Labovitz.pdf
Google, Akamai, RapidShare, …

## Slide 36: Question – What about IXPs
  Flattening of the AS topology
  What about IXPs impact
Google, Akamai, RapidShare, …
IXP

## Slide 37: Network map 2012+
  IXPs central component
  Lots of local peering – rich fabric
  Even flatter AS topology than assumed
„Hyper Giiants“
Large Content, Consumer, Hosting CDN
Global Transit/National Backbones
Global Internet Core
Regional / Tier2 Providers
AS 1
AS 2
IXP
IXP
IXP
Leaf IP Networks

## Slide 38: Some interesting observations (1)
Myth 1: Tier-1’s don’t public peer at IXPs
  Fact: All Tier-1’s are members at IXP and do public peering
    Tier-1’s typically use a “restrictive” peering policy
    Most IXP members use an “open” peering policy
Myth 2: Establishing peerings at IXPs is cumbersome
  Fact: Many IXPs make it very easy for its members to establish public peerings with other members
    „Handshake agreements“
    Use of IXP’s route server is offered as free value-added service
    Use of multi-lateral peering agreements
Myth 3: IXP peering links are for backup
  Fact: Most peering links at our IXP see traffic
    Most of the public peering links see traffic
    Does not include traffic on the private peering links at IXP

## Slide 39: Some interesting observations (2)
Myth 4: IXPs are not interesting
  Fact: As interesting as large ASes and big content
Myth 5: IXPs are very different from ASes
  Fact: Large IXPs start to look more and more like ASes
    Offering SLAs (DE-CIX in 2008, AMS-IX in 2011)
    Support for IXP resellers (e.g., AS43531 – IX Reach)
    Going oversees (AMS-IX starting a site in Hong Kong)
    Extensive monitoring capabilities
    IXP-specific traffic matrix vs. AS-specific traffic matrix

## Slide 40: Outline
Introduction to IXPs
A large European IXP
IXP peering fabric
IXP member diversity
IXP traffic matrix
Diversity
Discussion
Summary

## Slide 41: Summary
Large IXP study reveals diverse IXP eco-system wrt members, business types, connectivity, traffic, etc.
Large IXP supports rich peering fabric
  Single IXP doubles the estimated number of peering links
  Needs revamping of mental picture of AS-level Internet
Implications for studies of AS-level Internet
  ASes – can no longer be treated as „homogeneous“
  AS links – simple classification (peering, cust-prov) should fade
  IXP peerings – when peering links are used as cust-prov links…
  AS traffic – what traffic is carried by whom?

## Slide 42: Related work
Without IXP co-operation
  Connectivity related work
    Xu, Duan, Zhang, Chandrashekar: On Properties of Internet Exchange Points and their impact on AS Topology and Relationship, Networking, 2004
    Chang, Govindan, Jamin, Shenker, Willinger: Towards Capturing Representative AS-Level Internet Topologies. Computer Networks, 2004
    Chen, Choffnes, Potharaju, Chen, Bustamante, Pei, Zhao: Where the Sidewalk Ends: Extending the Internet AS Graph Using Traceroutes From P2P Users. ACM CoNEXT, 2009
    He, Siganos, Faloutsos, Krishnamurthy: A Systematic Framework for Unearthing the Missing Links: Measurements and Impact. NSDI, 2007
    Oliveira, Pei, Willinger, Zhang, Zhang: The (In)completeness of the Observed Internet AS-Level Structure. IEEE/ACM Trans. Networking, 2010
    Augustin, Krishnamurthy, Willinger: IXPs: Mapped? ACM IMC, 2009
  Traffic related work
    Restrepo, Stanojevic: A history of an Internet eXchange Point, CCR 2012
With IXP co-operation
  This work

## Slide 43: Summary
Large IXP study reveals diverse IXP eco-system wrt members, business types, connectivity, traffic, etc.
Large IXP supports rich peering fabric
  Single IXP doubles the estimated number of peering links
  Needs revamping of mental picture of AS-level Internet
Implications for studies of AS-level Internet
  ASes – can no longer be treated as „homogeneous“
  AS links – simple classification (peering, cust-prov) should fade
  IXP peerings – when peering links are used as cust-prov links…
  AS traffic – what traffic is carried by whom?